## Slide 1
Spider Webs and Sacrificial Failure
Impact regimes and quasi-static capacity

## Slide 2: Agenda
Single Thread Impact
Breaking Conditions
Numerical Simulations
Minimum Net Mass & Material Utilization
Surprise Bonus!

## Slide 3: Impact waves in single thread
Single infinite silk thread
How will the silk thread behave after impact?
What’s the critical speed to break the silk thread?
How will the stress in the silk thread change over time?
Notes: The analogy concerns particle motion relative to wave propagation. The physical mechanisms in rock and in a thread differ.
[Sources]
USGS, Body waves inside the earth
https://earthquake.usgs.gov/earthquakes/events/1906calif/18april/earthwaves.php
Illustrations: AI-generated conceptual schematics of P/S particle motion and the thread initial condition, based on the existing slide 5 setup.
[/Sources]

## Slide 4: Impact waves in single thread
Earthquake waves offer an analogy for thread impact. P waves are longitudinal: particle motion is parallel to propagation. S waves are transverse: particle motion is perpendicular to propagation.
Consider a thread initially at rest and unstrained. At x = 0, we suddenly impose a constant transverse velocity v₀. How does the thread respond?
How can transverse motion generate a longitudinal wave in the thread?
Notes: The analogy concerns particle motion relative to wave propagation. The physical mechanisms in rock and in a thread differ.
[Sources]
USGS, Body waves inside the earth
https://earthquake.usgs.gov/earthquakes/events/1906calif/18april/earthwaves.php
Illustrations: AI-generated conceptual schematics of P/S particle motion and the thread initial condition, based on the existing slide 5 setup.
[/Sources]

## Slide 5: Impact waves in single thread
Consider a long thread along x, at rest and unstrained, whose point x=0 is suddenly given a constant transverse velocity v0.
Before longitudinal wave
After longitudinal wave
Momentum change
Longitudinal Wave Velocity

## Slide 6: Impact waves in single thread
Mass conservation and thread tension determine the transverse wave speed.
Mass Conservation
Before longitudinal wave
After longitudinal wave
Thread deformation due to transversal wave.
Transversal Wave Velocity

## Slide 7: Impact waves in single thread
(Smith, 1958)
Pythagoras Theorem:
Having the approximations and , Smith equation become:
J. C. Smith, F. L. McCrackin, and H. F. Schiefer – “Stress-strain relationships in yarns subjected to rapid impact loading”, J. Res. Natl. Bur. Stand, 1958

## Slide 8: Thread breaking conditions
The thread breaks immediately at impact when the strain reaches (derived directly from Smith’s ):
Numerically we get for Silk and for Dyneema.
Material Constants
Silk
Dyneema

## Slide 9: Model material elasticity
Material Constants
Silk
Dyneema
We model the thread with the simplest law that captures strain stiffening, a linear term plus a cubic correction:
Dyneema fibers do not stiffen under tension. The stress-strain curve is nearly linear up to failure, at a strain of a few percent. For SK76, Sanborn et al. 2015 note that the response becomes increasingly linear as the strain rate increases.

## Slide 10: Single Thread - Simulation
Uniform Mesh
Segment length
Interior Nodes
0
Impact Node
1
Node 1
2
Node 2
interior chain
n-1
Node n-1
n
Anchored Node
Boundary Nodes (0 & n)
Explicit coordinate kinematic update.
Impact node kinematically driven; anchor fixed.
1. Position Advance
2. Evaluate Nodal Forces
Zero tension under compression ().
Nonlinear tension along segment unit vector.
Boundary conditions reapplied after acceleration step.
3. Velocity Advance

## Slide 11: Single Thread - Simulation
Numerical Stability
An explicit scheme is stable only if, in a single step, the wave does not travel further than one segment (the CFL condition):
For a small perturbation, the stiffness of a segment is the local slope. Therefore, the relevant speed is the tangent speed:
Single-thread transverse impact - analytical values versus numerical values from the above algorithm with 800 segments.

## Slide 12: Single Thread – Silk Simulation
Strain along the coordinate X measured from the impact point; dashed lines: , dotted lines:
Thread shape: the straight inclined segment between the impact point and the kink.

## Slide 13: Single Thread – Dyneema Simulation
Strain along the coordinate X measured from the impact point; dashed lines: , dotted lines:
Thread shape: the straight inclined segment between the impact point and the kink.

## Slide 14: Wave “ping-pong” effect
Finite Boundaries & Multiple Reflections:
Initial impact wave reaches frame anchors within microseconds
Reflected tension waves bounce between projectile and anchors dozens of times during arrest
Physical Takeaway:
The projectile does not experience isolated traveling wave fronts
The net behaves collectively as a quasi-static nonlinear spring assembly
Tension Homogenization:
Every time the wave bounces back and forth, the tension increases
Spatial stress gradients smooth out within milliseconds
Velocity Scale Disparity:
Transverse wave speed:
Drone impact velocity:

## Slide 15: From Wave PDE to Pure Geometry
Kinematic Strain Relation
Out-of-plane hub displacement w defines deformed length
Exact closed-form strain with prestrain :
Global Energy Balance
Total strain energy absorbed up to deflection w:

## Slide 16: Minimum Net Mass & Material Utilization
Equating drone kinetic energy to strain energy at failure
- Material utilization factor (structural efficiency)
For centered impact:
Specific energy to failure (J/kg), intrinsic material toughness
Hub impact remarkable independence
is completely independent of radial count N and radius R.

## Slide 17: Minimum Net Mass & Material Utilization
- Material utilization factor (structural efficiency)
For centered impact:

## Slide 18: Off-Centre Impact
Strain on the outer segment:

## Slide 19: Off-Centre Impact
After impact, the central node (hub) is at the coordinates .
Strain for the untouched radials:

## Slide 20: Off-Centre Impact
This cannot be solved analytically. We used the Nelder–Mead method (the simplex algorithm) to directly find the coordinates that minimize the function without computing the Hessian matrix.
Remember that hub-center impact was

## Slide 21: Off-Centre Impact – Thread Failure
Minimize 𝒰(h; w) until outer strain reaches ; store 𝒰(w1).
01 · First Rupture (w1)
Nelder-Mead
Severed outer segment is removed from the network connectivity matrix.
02 · Topology Pruning
Graph Update
Advance w past w1 with step size Δw (0.002R for S, 0.0005R for D).
03 · Deflection Step
Δw
Re-optimize hub coordinates across remaining radials at each step.
04 · Hub Re-equilibrium
min 𝒰rem
Identify when inner segment reaches ; extract 𝒰rem(w2).
05 · Second Rupture (w2)
Bisection
Sum total absorbed work WB and scale against theoretical capacity.
06 · Energy & Efficiency
Metric
Due to non-linear cubic elasticity and asymmetric hub shifts, energy absorption WB is resolved numerically via Nelder-Mead optimization and bisection.

## Slide 22: Off-Centre Impact
decrease of over 72% !
Indicator measures how much of the drone's kinetic energy exceeds the threshold of the first failure, relative to the useful capacity of the residual net
to leverage full sacrificial efficiency
Pure elastic response
Controlled sacrificial capture
Perforation / Catastrophic failure

## Slide 23: Limitations of the current approach
The cubic law has no yield region; real dragline silk softens before stiffening.
S. W. Cranford, A. Tarakanova, N. M. Pugno, and M. J. Buehler – “Nonlinear material behavior of spider silk yields robust Webs”, Nature 482, 72 (2012)
Threads are massless in the quasi-static analysis, and bending, friction at crossings, and knots are ignored.
, ignores threads mass.
Failure is instantaneous at , without damage or softening. A broken radial then fails at several segments as the released thread recoils.
Strength variability between threads, which drives cascades in fiber-bundle models is not included.
G. Pal et al. – “Scaling laws of failure dynamics on complex networks”, Sci. Rep. 13, 19733 (2023).